## Slide 1
DRIFT-SENSE
Navigation-Error Recovery for Wafer Inspection
Finding one site inside a sea of identical repeating cells — by measuring the geometry instead of searching it.
TEAM
Team name
«TEAM NAME»
Members & roles
«NAME — role», «NAME — role», «NAME — role»
College
«COLLEGE NAME»
Contact
«EMAIL» · «PHONE»
92.5%
accuracy where a non-periodic
landmark is in the field of view
0.10%
median error in the recovered
10x magnification
2.9s
per 1000x1000 image pair,
single CPU core
Applied Materials · i4C Hackathon · Problem Statement: Drift-Sense
Notes: Replace all «...» placeholders with real team details before submitting.

## Slide 2
2
Problem Statement Addressed
Selected: Drift-Sense — Navigation-Error Recovery
A wafer inspection tool must return to the same site thousands of times a day. Between visits the stage drifts — thermal expansion, fab-floor vibration, mechanical slack — and the tool lands several pixels away.
The tool cannot detect this from the landed image, because every die carries the same repeating layout: the structure at the wrong location looks almost identical to the right one.
Why it matters: if the tool cannot prove it is on the right cell, every measurement trended over time is comparing two different places on the die.
Classical template matching breaks down exactly where the layouts are most regular — DRAM arrays, FinFET gate fields.
In a 657x657px window at a 9px pitch, ~30 correlation peaks sit within 0.003 of the global maximum.
Choosing among them is not a matching problem. It is an identifiability problem.
Every cell is a valid-looking match. Only one is correct.

## Slide 3
3
Idea Description
Both architectures · classical, measurement-first localization · zero learned weights on the shipped path
ARCHITECTURE
Both DRAM and FinFET.
The generator renders word-line/bit-line grids with contact vias, and dense fin fields crossed by gate bars. Both are evaluated in every split, 50/50.
METHOD
Classical / geometric — by measurement.
Two learned alternatives were built and evaluated held-out. A CNN re-ranker scores 2.9% against 38.6% for the classical matched filter. A listwise learned ranker reaches 64.3% -> 67.1% (p = 0.69) — real, but not significant.
CORE IDEA
Measure the geometry; then discriminate.
The unknown ~10x magnification IS the ratio of the two lattice pitches. Measure it, and the search collapses from a blind sweep to a handful of geometrically permitted positions.
Why this beats template matching on periodic layouts
Template matching
Sweeps a scale band blindly, slides the template, takes the argmax of the correlation surface.
Drift-Sense
Measures magnification and rotation from the spectrum, spectrally subtracts the lattice so only aperiodic landmarks remain, then makes the surviving candidates compete against each other.

## Slide 4
4
Proposed Solution
Dataset generator (left) and localization pipeline (right) — every augmentation cited, see slide 9
Dataset generator · dataset_generator.py
--style {dram,finfet,both} --n --out --difficulty-mix --placement --noise-scale --pitch-shift
Scene rendered supersampled, then area-averaged down 10x — demagnification without aliasing.
Imaging chain in physical order: edge brightening → astigmatic PSF → scan distortion → charging → shading → sensor noise.
Independent Poisson + Gaussian draw per capture; search side uniformly noisier than reference.
Rotation applied to the reference crop only — rotating the search canvas silently corrupts ground truth.
Aperiodic landmarks injected deliberately: array corner, dropped/doubled via, gate crossing.
Ground truth records the true centre AND whether the site is identifiable at all.
Localization · localize.py
python localize.py reference.png search.png → "x, y"
1
Lattice sensor
2-D spectrum → pitch, orientation. Magnification = pitch ratio, measured to 0.10%.
2
Rotation + phase lock
Sub-bin multi-harmonic angle (0.15°). Cross-image phase pins the centre modulo the pitch.
3
Aperiodic residual
Spectral notch deletes the lattice. Only landmarks survive — the sole channel carrying absolute identity.
4
Propose
Decimated multi-scale NCC over the full frame, plus residual peaks. Cheap, and only ever proposes.
5
Rescore at full res
Candidate crops upsampled to reference resolution — decided where cells actually differ.
6
Decide
Landmark evidence judges. The mandated centre rule breaks genuine ties only.

## Slide 5
5
Innovation & Uniqueness
Four things a stronger backbone would not have given us
1
The 10x scale is measured, not searched
The ratio of the two lattice pitches IS the unknown magnification. A blind 8-point sweep over 8.3–11.7 becomes a tight measured bracket, so the reference footprint lands within ~1px of truth.
2
The lattice is spectrally subtracted before matching
Correlating the two aperiodic residuals isolates exactly the content that carries absolute identity. This is also what makes honest abstention possible: in a true array interior the channel is flat by construction.
3
Candidates compete instead of being scored alone
Beliefs are normalised across the candidate set, and a lattice-phase consensus term scores each candidate against the phase the others agree on — information invisible to any per-patch classifier.
4
Spatial induction: making the lattice prove its own geometry
The pitch is tested the way one proves a statement over the integers — if pitch p is real, lag n·p must also be a peak. Catches 13 / 13 silent lattice failures at zero false alarms, and predicts solvability (r = -0.346, p = 0.00043).
And one meta-choice: every idea measured that did NOT pay is documented rather than deleted — the centre-distance prior, the phase penalty, the calibrated commit gate, induction as a scale gate, and the CNN re-ranker (held-out: right on 0 trials the classical fusion gets wrong, so the weight sweep picks 0).

## Slide 6
6
Results
100 randomized pairs, uniform placement, 50/50 DRAM/FinFET — produced by benchmark.py
49.0%
within 15px
all 100 pairs
61.2%
within 15px
identifiable pairs
37.0%
within 5px
all 100 pairs
2.9s
per pair
1000x1000, 1 CPU core
Accuracy is set by what is in the field of view — not by architecture
92.5%
Array corner
42.1%
Gate crossing
19.0%
Single via defect
0%
No landmark in FOV
SUCCESS — array corner in FOV, error 0.4px
HONEST FAILURE — defect-free array interior, error 320.5px, and confidence 0.85: wrong AND sure.
Notes: A DRAM reference footprint spans ~78 lattice cells and a dropped via alters exactly one of them -- roughly 1.3% of the content separating the true site from its lattice-shifted rival. 87.5% of identifiable sites ARE correctly proposed by the candidate stage; the loss is in ranking them, not in finding them.

## Slide 7
7
Technology & Feasibility
Torch-free inference — a reviewer installs four packages and runs one command
Language / stack
Python 3.12 · NumPy · OpenCV · SciPy · Pillow. No GPU, no learned weights on the shipped path.
Hardware used
Development and every benchmark on a single consumer CPU core. No cloud, no accelerator.
Dataset generation
~200s per 100 pairs for a 100-pair split (1000x1000 reference + 1000x1000 search, supersampled render).
Inference per pair
2.9s mean, 7.1s worst case, for a 1000x1000 pair on one CPU core.
Model size
0 bytes. The shipped path carries no weights. The unvalidated research re-ranker is a 32-d Siamese CNN (136 KB).
Reproducibility
requirements.txt is the complete pip freeze; requirements-inference.txt is the 4-package torch-free subset.
Robustness measured, not assumed: no measurable loss at 2x or 3x search-side sensor noise, though accuracy does fall away from the tuned lattice-pitch band — the spectral front end does not degrade the way a pixel-domain matcher would.

## Slide 8
Repository & Demo
GITHUB (mandatory)
«https://github.com/«USER»/drift-sense»
Public repository — generator, inference script, benchmarks, probes, citations.
VIDEO (optional)
«LINK — algorithm running on one sample pair»
Recommended: show localize.py run end-to-end on a fresh pair.
What a reviewer runs, with no manual edits:
pip install -r requirements-inference.txt
python localize.py reference.png search.png
Notes: Replace both «...» placeholders with the real URLs before submitting.

## Slide 9
9
References
Per-choice justification in CITATIONS.md — 15 sections covering every augmentation and structural parameter
SEM image formation
Goldstein, J. et al. Scanning Electron Microscopy and X-Ray Microanalysis (edge effect; charging; detector collection efficiency).
Reimer, L. (1998). Scanning Electron Microscopy: Physics of Image Formation and Microanalysis, 2nd ed., Springer.
Cazaux, J. (2004). Charging in scanning electron microscopy from inside and outside the specimen.
Erasmus, S. J. & Smith, K. C. A. (1982). An automatic focusing and astigmatism correction system for the SEM.
Noise modelling
Zhang, Y. et al. (2019). A Poisson-Gaussian Denoising Dataset with Real Fluorescence Microscopy Images, CVPR.
Foi, A. et al. (2008). Practical Poissonian-Gaussian noise modeling for raw-data images.
Healey, G. E. & Kondepudy, R. (1994). Radiometric CCD camera calibration and noise estimation.
Janesick, J. R. (2001). Scientific Charge-Coupled Devices, SPIE Press.
Device structure & pitch
imec, DRAM peripheral transistors technology platform.
SemiAnalysis, The Memory Wall: Past, Present and Future of DRAM (pitch / feature-size / cell-area).
ASIC North, FinFET Technology and Layout, Part 1 (fin pitch, contacted poly pitch).
Sicard, E. Introducing 5-nm FinFET technology (fin and gate pitches by node).
Bunday, B. D. et al., fin/gate metrology dimensions (arXiv:1503.06617, Table 10).
Localization & the ambiguity problem
Lewis, J. P. (1995). Fast Normalized Cross-Correlation, Vision Interface.
US Patent 9,430,457 — Ambiguity reduction for image alignment applications.
US Patent 11,481,922 — Online navigational drift correction for metrology measurements.
Reddy, B. S. & Chatterji, B. N. (1996). An FFT-based technique for translation, rotation and scale-invariant registration.
Foroosh, H. et al. (2002). Extension of phase correlation to subpixel registration.
Mack, C. (2007). Fundamental Principles of Optical Lithography; Levinson, H. J. (2010). Principles of Lithography.